## Slide 1
Crowd Supply
Course Workbook

## Slide 2: Table of Contents
About this Workbook | Slide 3
Pre-Lab: Workshop Pre-requisites | Slide 4
Lab : Implementing the Vivado Design | Slide 7

## Slide 3: About this Workbook
This workbook is designed to be used in conjunction with the Crowd Supply lab one workshop.
The contents of this workbook are created by Adiuvo Engineering & Training, Ltd.
If you have any questions about the contents, or need assistance, please contact Adam Taylor at adam@adiuvoengineering.com.

## Slide 4: Pre-Lab Workshop Pre-requisites

## Slide 5: Required Hardware
Pre-Lab
The following hardware is required to complete this series of labs
Digilent Basys3 Development board

## Slide 6: Downloads and Installations
Vitis 2020.2 – Includes Vivado | Download
Source Project Files | Download
Pre-Lab
Step 1 – Download and install the following at least one day prior to the workshop. This may take a significant amount of time and drive space.

## Slide 7: Lab Creating Pong on the Basys3

## Slide 8: Crowd Supply: Lab One
Step 1 – Picking up from last time we had just generated the bit stream. Now we need to export it, with the Vivado project open from the file menu select export hardware
Lab One

## Slide 9: Crowd Supply: Lab One
Step 1 – Select include bitstream
Lab One

## Slide 10: Crowd Supply: Lab One
Step 1 – Leave the defaults unchanged and click next
Lab One

## Slide 11: Crowd Supply: Lab One
Step 1 – Click finish to export the hardware definition
Lab One

## Slide 12: Crowd Supply: Lab One
Step 1 – From the Vivado Tools menu select launch Vitis, at the pop up dialog select browse
Lab One

## Slide 13: Crowd Supply: Lab One
Step 1 – Create a new folder called wksp within the Vivado Project
Lab One

## Slide 14: Crowd Supply: Lab One
Step 1 – Select create application
Lab One

## Slide 15: Crowd Supply: Lab One
Step 1 – Click on next
Lab One

## Slide 16: Crowd Supply: Lab One
Step 1 – Select “create a new platform from hardware (XSA)” and click browse
Lab One

## Slide 17: Crowd Supply: Lab One
Step 1 – Navigate to the location of the XSA we just exported from Vivado, click Open
Lab One

## Slide 18: Crowd Supply: Lab One
Step 1 – Click OK to use this as the platform
Lab One

## Slide 19: Crowd Supply: Lab One
Step 1 – Enter a project name and click next
Lab One

## Slide 20: Crowd Supply: Lab One
Step 1 – Leave the domains unchanged, clicked next
Lab One

## Slide 21: Crowd Supply: Lab One
Step 1 – Select the hello world project click next
Lab One

## Slide 22: Crowd Supply: Lab One
Step 1 – You will see a project be created as below – Connect the Basys3 to the development system using the USB cable and turn on the board
Lab One

## Slide 23: Crowd Supply: Lab One
Step 1 – In the assistant window select the project, right click on release and from the Debug menu select launch on Hardware
Lab One

## Slide 24: Crowd Supply: Lab One
Step 1 – Open a terminal window (9600N1) when the debug is loaded single step through the design, and you will see the hello world in the terminal. This proves the MicroBlaze is working all OK so we can start with the application development.
Lab One

## Slide 25: Crowd Supply: Lab One
Step 1 – Clone the repository with the command
git clone https://github.com/ATaylorCEngFIET/CrowdSupplyWorkShop2
Lab One

## Slide 26: Crowd Supply: Lab One
Step 1 – This will clone two source files from the repo – copy both these files
Lab One

## Slide 27: Crowd Supply: Lab One
Step 1 – Copy them into the wksp files under the src for the previously created project
Lab One

## Slide 28: Crowd Supply: Lab One
Step 1 – If prompted allow the helloworld.c file to be replaced
Lab One

## Slide 29: Crowd Supply: Lab One
Step 1 – The Vitis project should now show, the new files we just copied in – click build project on the hammer
Lab One

## Slide 30: Crowd Supply: Lab One
Step 1 – Open Vivado 2020.2. Once Vivado opens, open the Xhub Store
Lab One

## Slide 31: Crowd Supply: Lab One
Step 1 – Open Vivado 2020.2. Once Vivado opens, open the Xhub Store
Lab One

## Slide 32: Crowd Supply: Lab One
Step 1 – Once the build competes re-run the debug on hardware –with a VGA monitor attached, click on run – after a few seconds you should see the game appear on the screen
Lab One

## Slide 33: Crowd Supply: Lab One
Step 1 – Expand the Binaries and you will see the ELF file which is running on the MicroBlaze – To use this on the board from power up we need to include it in the bitstream
Lab One

## Slide 34: Crowd Supply: Lab One
Step 1 – Switch back to Vivado
Lab One

## Slide 35: Crowd Supply: Lab One
Step 1 – From the Tools menu select Associate ELF File
Lab One

## Slide 36: Crowd Supply: Lab One
Step 1 – Select … on the MicroBlaze design sources
Lab One

## Slide 37: Crowd Supply: Lab One
Step 1 – Click Add Files and select the ELF from Vitis Project we just created
Lab One

## Slide 38: Crowd Supply: Lab One
Step 1 – Select the PONG file
Lab One

## Slide 39: Crowd Supply: Lab One
Step 1 – Select the design settings
Lab One

## Slide 40: Crowd Supply: Lab One
Step 1 – In the settings under bitstream select –bin_file
Lab One

## Slide 41: Crowd Supply: Lab One
Step 1 – Rerun the bit stream generation and when it completes select open hardware manager
Lab One

## Slide 42: Crowd Supply: Lab One
Step 1 – When the hardware manager opens select Open Target and Auto Connect
Lab One

## Slide 43: Crowd Supply: Lab One
Step 1 – Select add configuration memory device
Lab One

## Slide 44: Crowd Supply: Lab One
Step 1 – Select the appropriate memory device depending on the QSPI fitted
Lab One

## Slide 45: Crowd Supply: Lab One
Step 1 – When prompted if you want to configure a memory device now click OK
Lab One

## Slide 46: Crowd Supply: Lab One
Step 1 – Select the BIN file just created from under the Vivado Project Runs / Implementation directory
Lab One

## Slide 47: Crowd Supply: Lab One
Step 1 – Click OK to start the programming of the flash – ensure the power is not disrupted while the write takes place
Lab One

## Slide 48: Crowd Supply: Lab One
Step 1 – Once the flash is finished click OK, Close the hardware manager and the Vivado project.
Lab One